## Slide 1
Energy system modelling using OSeMOSYS
LECTURE 14
MODEL CALIBRATION AND SCENARIO VALIDATION

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO1: Understand the concept of model calibration.
ILO2: Learn the basic steps and parameters used to calibrate an OSeMOSYS model.
ILO3: Identify additional parameters necessary for an accurate representation of an energy system.

## Slide 3
14.1.1 What is model calibration about?
14.1 Basic steps in model calibration
Model calibration refers to the process of adjusting model parameters to ensure that outputs align with historical real-world data
Chart: Final energy consumption 2021
| Biomass | Natural gas | Diesel | Gasoline | LPG | Electricity
Real data | 59 | 19 | 70 | 85 | 36 | 123
Model | 57 | 19 | 64 | 83 | 34 | 119
Chart: Primary energy production
| Biomass | Natural gas | Crude oil | Hydro | Solar | Wind
Real data | 59 | 19 | 241 | 89 | 23 | 11
Model | 58 | 20 | 239 | 87 | 25 | 9
Chart: Carbon dioxide emissions
| Real data | Model
 | 75 | 73
Notes: Model calibration involves adjusting parameters to ensure that the model's outputs align with historical real-world data. In the case of OSeMOSYS, an optimization-based mathematical model, the goal is to produce an optimal solution rather than the most probable one. Calibration, in this context, focuses on replicating historical energy production and consumption patterns.
To achieve this, it is considered best practice to select one or more years with reliable historical data as calibration years. Additionally, as sustainability becomes a key criterion in energy planning, emissions should also be incorporated into the calibration process.However, we primarily calibrate energy production and capacity while conducting a sense-check on emissions. Since emissions are a direct consequence of energy production and use, properly calibrating energy production and consumption should result in aligned emission levels. This is because fossil fuel combustion—and its associated emissions—is directly proportional to energy use.
The slide presents an example of how the three main aspects—energy production, consumption, and emissions—can be compared between real-world data and model outputs to verify appropriate calibration.

## Slide 4
4
14.1.2 Residual capacity
14.1 Basic steps in model calibration
Calibration years (known data) |  |  |  | Constant value from last year (assumption 1) |  |  |  | 
2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
30 | 32 | 35 | 36 | 36 | 36 | 36 | 36 | 36
Linear decrease considering operational life of 6 years (assumption 2) |  |  |  |  |  | Residual capacity is zero for the rest of the years |  | 
2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038
30 | 24 | 18 | 12 | 6 | 0 | 0 | 0 | 0
Chart: Residual Capacity (MW)
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038
 | 30 | 32 | 35 | 36 | 36 | 36 | 36 | 36 | 36 | 30 | 24 | 18 | 12 | 6 | 0 | 0 | 0 | 0
Projected
Historical
Existing capacity available each year before the modelling period.
Notes: While the future remains uncertain, the existing capacity and prior performance of energy systems can offer insights into future behavior. It’s important to remember that existing or installed capacity for each year is defined by the Residual Capacity parameter. Collecting accurate data on residual capacity is a crucial first step in model calibration.
For historical years, this data is relatively accurate if reliable sources are used. However, a key question arises: What is the expected decommissioning of existing capacity in future years?
In the power sector, where individual power plants can be identified and decommissioning schedules are often available, estimating future residual capacity is straightforward. For example, if the current capacity is 600 MW in 2026 and a 50 MW plant is decommissioned in 2027, the residual capacity for 2027 would be 600 - 50 = 550 MW.
In contrast, for technologies like stoves, boilers, or vehicles, estimating changes in residual capacity over time is more challenging. A simple approach is to assume a status quo, keeping residual capacity constant for a few years (e.g., 3–5 years) before reducing it linearly based on the technology's operational life. For instance, if a stove has an operational life of 10 years, its residual capacity could be decreased in 10 equal steps until it reaches zero.
The figure on the slide illustrates an example of how residual capacity might be estimated over time.

## Slide 5
5
14.1.3 Total Technology Annual Activity Lower Limit
14.1 Basic steps in model calibration
Calibration years (known data) |  |  |  | Constant value from last year (assumption 1) |  |  |  | 
2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
26 | 28 | 29 | 32 | 32 | 32 | 32 | 32 | 32
Linear decrease considering operational life of 6 years (assumption 2) |  |  |  |  |  | Residual capacity is zero for the rest of the years |  | 
2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038
27 | 22 | 17 | 12 | 7 | 0 | 0 | 0 | 0
Chart: Energy production - Total Technology Annual Activity Lower Limit (PJ)
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038
 | 26 | 28 | 29 | 32 | 32 | 32 | 32 | 32 | 32 | 27 | 22 | 17 | 12 | 7 | 0 | 0 | 0 | 0
Projected
Historical
Total minimum level of activity allowed for a technology in one year.
Notes: In previous hands-on exercises, we observed situations where residual capacities were entirely unused. Instead, the model opted to install new capacities for various technologies, disregarding the existing ones. We also noted instances where a capacity was fully utilized in one year but abruptly became unused in the immediate next year.
This behavior reflects the nature of OSeMOSYS as an optimization model. It aims to determine the least-cost solution for energy production and usage while neglecting certain practical realities of energy systems. To avoid such unrealistic outcomes, we need to calibrate energy production for each sector.
Calibration is achieved by employing the Total Technology Annual Activity Lower Limit parameter. This parameter ensures that a technology produces at least a specified minimum amount of energy in a given year. For instance, if the biomass stove technology has a lower limit set to 20 PJ in 2023, the model will generate an outcome where biomass stoves produce at least 20 PJ of cooking service in that year. While the technology may produce more than 20 PJ, the parameter guarantees a minimum production level without restricting maximum output.
Historical production data, such as electricity, heat, or other energy services, can be sourced from final energy balances or sector-specific reports. This historical data serves as the baseline for calibrating future energy production.
The challenge arises when predicting the energy production of existing capacities in future years. Similar to the approach for residual capacity, we can assume that energy production remains constant for a few years ahead and then decreases linearly based on the operational life of the technology. This approach aligns the expected energy production with the lifespan and decommissioning of the capacity.
It is crucial to apply consistent assumptions for both residual capacity and energy production. Since energy production is directly proportional to existing capacity, any assumptions regarding one should be mirrored in the other.
The figure on the slide demonstrates an example of how energy production can be estimated over time, using a combination of constant production in the short term and a gradual decline based on operational life.

## Slide 6
6
14.1.4 Total Annual Max Capacity Investment
14.1 Basic steps in model calibration
Maximum new capacity allowed for a technology in one year.
The default value is 999,999, which represents no constraint on the new installed capacity for a technology.
By setting this parameter to zero during the calibration years, we deactivate technologies that are not part of the energy mix in the historical data.
Technology | Calibration years (known data) |  |  |  | Optimized modelling period |  |  |  | 
 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Coal power plant | 999999 | 999999 | 999999 | 999999 | 999999 | 999999 | 999999 | 999999 | 999999
Geothermal power plant | 0 | 0 | 0 | 0 | 999999 | 999999 | 999999 | 999999 | 999999
Example of how to parametrize a current technology in the mix (coal power plant) and a potential technology for the future (geothermal power plant)
Notes: During the calibration years, we add all existing capacities and energy productions to replicate the expected historical behavior. At the same time, we ensure that technologies not included in the energy mix during those years are not installed.
To achieve this, we use the parameter Total Annual Max Capacity Investment, which sets the maximum new capacity that can be installed for a technology per year. For example, if this parameter is set to 1 GW, the maximum new capacity installed in that year cannot exceed 1 GW. Setting the parameter to zero effectively deactivates any new capacity for that technology.
By setting Total Annual Max Capacity Investment to zero during the calibration years for all new technologies, we ensure the energy mix aligns with historical data. However, it’s crucial to restrict this parameter to the calibration years only; otherwise, these technologies will be unable to compete in future scenarios. It is also advisable to set this parameter to zero for a few years beyond the last calibration year for technologies with long construction periods. For example, it is unlikely that an energy planner would propose a hydropower plant to be installed between 2024 and 2025, given that such plants typically require 5 to 10 years to build.

## Slide 7
7
Lecture 14.1 References
KTH. (2018). OSeMOSYS Documentation. https://osemosys.readthedocs.io/en/latest/index.html#
Plazas-Niño, F. (2024). Step-by-Step Guide to National Energy System Modelling with OSeMOSYS (v1.0). Zenodo. https://doi.org/10.5281/zenodo.13883416

## Slide 8
8
14.2.1 Technology penetration rate
There are two methods to introduce a technology penetration rate:
Total Annual Max Capacity Investment: This parameter limits the maximum new capacity that can be installed each year.
Technology Activity Increase By Mode Limit: This parameter limits the maximum percentage increase in activity that a technology can achieve each year.
A penetration rate helps prevent abrupt jumps in technology utilization.
14.2 Scenario validation
Notes: Another common behavior observed in optimization results is the sudden jump in installed capacities from one year to the next when a technology becomes significantly cheaper than another in supplying an energy service. In reality, it is nearly impossible to decommission all installed capacity of one technology in a single year to make way for a new one.
To address this, we can incorporate a technology penetration rate using two approaches:
Total Annual Max Capacity Investment: This parameter sets a limit on the maximum new capacity that can be installed each year, based on historical data and market projections. For instance, if the power mix has been growing at an average rate of 1.2 GW per year, this value or a percentage of it could be used to regulate the penetration of new technologies in future years.
Technology Activity Increase By Mode Limit: This parameter limits the annual growth in activity levels for a technology to a specified percentage. For example, if a power plant generates 20 PJ in 2023 and the parameter is set to 0.1 (10%), the maximum generation in 2024 would be capped at 22 PJ (10% of 20 is 2, so 20 + 2 = 22). The percentage increase can be derived from historical trends or sectoral reports.
By applying these parameters, we can create a more realistic representation of technology transitions in energy systems.

## Slide 9
9
14.2.2 Total Annual Min Capacity Investment
14.2 Scenario validation
Minimum new capacity of a technology to be installed, expressed in power units.
We can use this parameter to account for all future energy projects confirmed to come online within the modeling horizon.
For example, a new solar plant with a capacity of 0.2 GW planned to be in operation in 2025.
Notes: In some cases, significant projects such as power plants or industrial facilities are under construction and expected to come online within the next few years. When detailed information about these projects—such as capacity, technology type, and start year—is available, we can integrate this data into the model.
To account for these capacities, we use the parameter ‘Total Annual Min Capacity Investment.’ For each technology and the corresponding year, the value of the New Planned Installed Capacity is specified. For instance, if a solar PV power plant with a capacity of 0.2 GW is under construction and scheduled to become operational in 2025, we would input a value of 0.2 for the year 2025 under the technology code PWRSOL. This approach can be applied to any type of technology. However, it’s important to ensure that the capacity being included is significant and its operation is confirmed.
For newly planned capacities, it is also possible to set an expected level of production based on the installed capacity. Since this is a fixed new capacity, its potential energy production can often be assumed to remain constant throughout its operational life.
For example, a new natural gas power plant with a capacity of 0.1 GW planned for 2025 could generate approximately 2.5 PJ per year. If the plant has an operational life of 25 years, we could set the parameter ‘Total Technology Annual Activity Lower Limit’ to 2.5 PJ for each year from 2025 to 2049.
If there is no requirement to define a minimum production level for the new facility, this step can be omitted. By leaving the production unconstrained, the model can determine whether the plant becomes a stranded asset—unused capacity in the optimized system.
When adding data for Total Annual Min Capacity Investment, it is essential to ensure that the values are equal to or below the Total Annual Max Capacity Investment. Setting a minimum level higher than the maximum will result in an infeasible solution.

## Slide 10
14.2.3 Total Technology Model Period Activity Upper Limit
14.2 Scenario validation
Total maximum level of activity allowed for a technology in the entire modelled period. It represents the total reserves of fossil fuels.
Crude oil
Natural gas
Coal
Nuclear fuels
Notes: Energy systems cannot produce energy infinitely. For fossil fuels, it is crucial to specify the reserves available for each type of fuel, including crude oil, natural gas, coal, and nuclear fuels. These reserve data are typically reported in weight or volume terms and must be converted into energy units. For example, 1 million barrels of oil is approximately 6 PJ.
To represent this in the model, we use the parameter Total Technology Annual Activity Upper Limit. This parameter sets a maximum limit on energy production for the entire modelling period.

## Slide 11
14.2.4 Total Technology Annual Activity Upper Limit
14.2 Scenario validation
Total maximum level of activity allowed for a technology in one year. It represents the technical potential of energy production of a technology.
Fossil fuels
Renewables
Controlled by depletion features in each reservoir or mine.
Controlled by natural conditions of each region
This parameter is defined for primary energy technologies such as MINCOA or MINBIO.
Notes: For fossil fuels, annual energy production cannot increase disproportionately from one year to the next. Oil reservoirs and coal mines have maximum production levels dictated by their depletion characteristics. However, detailed data on these limits is often unavailable, making it difficult to calculate an accurate average for an aggregated technology representing fuel extraction.
A simple approach is to use historical production data, taking the highest value as the default for the early years of the modeling period. This maximum can then increase linearly by a reasonable percentage over time. Adjustments can also be made if there is data on the development of new reservoirs or mines expected to become commercially viable in the future.
For renewables, the annual maximum potential is determined by the region or country’s natural conditions. For example, wind speed directly impacts the energy generated by wind power plants, typically referred to as the technical potential of the energy source.
In both cases—fossil fuels and renewables—the maximum annual energy production is defined using the Total Technology Annual Activity Upper Limit parameter. We add this parameter for primary energy source technologies (e.g., MINNGS, MINCOA, MINSOL, MINHYD)

## Slide 12
14.2.5 Total Annual Max Capacity
14.2 Scenario validation
Total maximum (residual plus cumulatively new installed) capacity allowed for a technology in a specified year. Specially used for renewable power plant technologies.
This parameter is defined for power plant technologies such as PWRSOL or PWRWND.
Solar
Wind
Hydro
Geothermal
Notes: For renewable energy sources, the technical potential may sometimes be expressed in capacity units (GW) rather than energy production (PJ). For example, reports may estimate a maximum installed capacity of 30 GW for photovoltaic solar power plants. This upper limit on total possible installed capacity can be used instead of the maximum energy production discussed on the previous slide.
In such cases, the parameter Total Annual Max Capacity is used. This parameter sets a maximum limit on the total installed capacity, including both residual (pre-existing) capacity and new cumulative capacity.
It is important to note that this parameter is applied to power plant technologies, not primary energy sources.

## Slide 13
13
Lecture 14.2 References
KTH. (2018). OSeMOSYS Documentation. https://osemosys.readthedocs.io/en/latest/index.html#
Plazas-Niño, F. (2024). Step-by-Step Guide to National Energy System Modelling with OSeMOSYS (v1.0). Zenodo. https://doi.org/10.5281/zenodo.13883416

## Slide 14: Thank you
www.climatecompatiblegrowth.com