## Slide 1: 6. Households
Notes: Licence: This work is licensed under the Creative Commons Attribution 4.0 International License (CC BY 4.0). To view a copy of this license, visit https://creativecommons.org/licenses/by/4.0/.
Attribution: Please cite as: Kiley, F. (2025) An Introduction to Simulating Energy Demand with MAED. Version 1. Climate Compatible Growth Teaching Kit Website, Climate Compatible Growth.

## Slide 2: Contents
6.1 Structure in MAED
6.2 Equations
6.3 Data Processing and Input

## Slide 3: 6.1 Structure in MAED

## Slide 4: MAED Sectors
Energy consumer sector
Economic sector
(GDP structure)
Industry
Agriculture
Transport
Household
Services
Construction
Mining
Manufacturing
Service (including transport)
Energy

## Slide 5: Subsector Definition
More detail possible if data allows
BUT
Energy balances rarely distinguish between urban and rural consumption
Complimentary data can fill gaps: household surveys, census, other national studies/surveys.
Higher detail enables more accurate modelling of energy consumption patterns
BUT don’t overcomplicate if not necessary
Household
Urban
Rural
…
…
…
…
…
…

## Slide 6: End Uses in Household

## Slide 7: Structure
Urban
Rural
Specific Electricity Uses
Cooking
Air Conditioning
Electricity
Heat Pump
Traditional Fuels
Modern Biomass
Fossil Fuels
Solar Thermal
District Heat
End Use
Energy Carrier
Water Heating
Space Heating

## Slide 8: 6.2 Equations

## Slide 9: Household Equations
Number of Households
Number of Dwellings in urban or rural areas
Total population
Fraction of population in urban or rural areas
Persons per household in urban or rural areas

## Slide 10: Household Equations
Space Heating
Useful energy demand for space heating
Number of dwellings
Fraction of dwellings of type i
Fraction of dwellings requiring space heating
Size of dwelling of type i
Floor area actually heated in dwelling type i
Heat loss rate
Degree days

## Slide 11: Household Equations
Degree Days
MAT (Monthly Average Temperature)
18oC
ND Number of days per month
31 28 31 30 31 30 31 31 30 31 30 31
Only for months when MAT is less than 18 (yellow)

## Slide 12: Household Equations
Heat Transfer Coefficient of Buildings, K Value
Typical figures for the heat transfer coefficient (Wh/sqm/°C/h), depending on the material composition and insulation method:
Building element Wh/sqm/°C/h
Solid 225 mm brick wall 2.0
Wall, Internal insulation 0.45 - 0.48
Wall, External insulation 0.44
Wall, Cavity insulation 0.19 - 0.40
Straw-bale wall 0.13
Window, Single glazing 5.6
Window, Double glazing 2.8
Window, Double glazing, with Argon 2.6
Window, Double glazing, Low-E 1.8
Window, Double glazing, Low-E with Argon 1.5
Roof 0.16 - 0.25
Floor 0.45

## Slide 13: Household Equations
Water Heating
Useful energy demand for water heating
Number of dwellings
Persons per household
Fraction of dwellings with hot water facilities
Specific Hot water energy consumption per person

## Slide 14: Household Equations
Cooking
Useful energy demand for cooking
Number of dwellings
Specific energy consumption for cooking

## Slide 15: Household Equations
Air Conditioning
Useful energy demand for air conditioning
Number of dwellings
Fraction of dwellings of type i
Fraction of dwellings with air conditioning
Specific cooling requirements

## Slide 16: Household Equations
Appliances and Lighting
Final energy demand for appliances/lighting by electricity
Total number of dwellings
Fraction of electrified dwellings
Specific electricity consumption for appliance/lighting
Final energy demand for appliances/lighting by fossil fuels
Specific fossil fuel consumption for appliances/lighting

## Slide 17: Household Equations
Useful to Final: Space Heating, Water Heating, Cooking
District Heating
Solar Thermal
Traditional Fuels
Modern Biomass

## Slide 18: Household Equations
Useful to Final: Space Heating, Water Heating, Cooking continued
If PEN Heat Pumps >0…
Electricity
Coefficient of performance
Fossil Fuels
Approximate share of space heating (SH) demand in households that can be met with solar installations. The rest of the demand will have to be met by a backup system.
Penetration of solar thermal in space heating

## Slide 19: Household Equations
Useful to Final: Air Conditioning
Electricity
Fossil Fuels

## Slide 20: 6.3 Data Processing and Input

## Slide 21: Input Data
Shares by type of dwelling (%)
Average house size (m 2 )
Specific requirements per person in useful energy (energy/ cap /year)
Percentage of homes with water heating systems (%)
Participation of energy sources within useful energy (%)
Energy efficiency (%)
water heating
Specific requirements for houses in useful energy (energy/ dwelling /year)
Participation of energy sources within useful energy (%)
Energy efficiency (%)
Cooking
Heat losses rate per dwelling (Wh/m2/C/h)
Percentage of houses with heating (%)
Participation of energy sources within useful energy (%)
Energy efficiency (%)
Heating

## Slide 22: Continued…
Specific requirements for houses in useful energy (energy/ dwelling /year)
Percentage of homes with air conditioning systems (%)
COP
Air-conditioning
Electrification rate (%)
Specific electricity requirements for equipment per dwelling (energy/ dwelling /year)
Specific electricity requirements for lighting per dwelling (energy/ dwelling /year)
Specific uses of electricity and lighting
The Urban and Rural sectors are modeled the same, so the explanations given below are valid for all houses of the two subsectors.

## Slide 23: Data Processing
Divide by end uses: census/ survey results or expert judgment can be used
N.B. In the MAED UI, when dealing with energy units other than GWyr, a conversion factor needs to be used for your Final Energy Demand e.g. if using Energy Units of PJ, final energy demands derived from an energy balance need to be converted to PJh (multiply PJ value by 8760) and the Useful Energy Demand and Energy Intensity calculated from that value.
GWh

## Slide 24
Divide by Household type

## Slide 25: Water Heating
Calculate the specific requirements per person in useful energy (energy / cap / year)

## Slide 26: Cooking
Calculate the specific requirements per house in useful energy (energy/ dwelling /year)

## Slide 27: Space Heating
Calculate heat losses by type of dwelling ( Wh / m2 /°C/h)

## Slide 28: Air Conditioning
Calculate the specific requirements per household in useful energy (energy/ dwelling /year)
Number of homes with air conditioning
COP
Efficiency ( Coefficient of performance)

## Slide 29: Appliances and Lighting
Calculate the number of electrified homes
Electrification percentage
Calculate the specific consumption of electricity (ELAPDW) / lighting (LIGHTDW) per household

## Slide 30: Thank you
www.climatecompatiblegrowth.com