## Slide 1
LECTURE 7 TRANSPORT AND SERVICE SECTORS
Version 2.0
Model for Analysis of Energy Demand
Notes: Licence: This work is licensed under the Creative Commons Attribution 4.0 International License (CC BY 4.0). To view a copy of this license, visit https://creativecommons.org/licenses/by/4.0/.
Attribution: Please cite as: Kiley, F. (2025) An Introduction to Simulating Energy Demand with MAED. Version 1. Climate Compatible Growth Teaching Kit Website, Climate Compatible Growth.

## Slide 2: Intended Learning Outcomes (ILOs)
7.1 Service Sector and its sub-sectors
7.2 Base Year Reconstruction - Collection of Raw Data
7.3 Transport Sector and its sub-sectors
2
This lecture has four Intended Learning Outcomes (ILOs):
ILO1: learn about the service sector and its subsectors
ILO2: learn how to collect the raw data needed for the base year reconstruction
ILO3: learn about the transport sector and its subsectors
Notes: This lecture has four Intended Learner Outcomes: to learn about the service sector and its subsector, how to collect the raw data for the base year reconstruction and about the transport sector.

## Slide 3
3
Lecture 7.1 Service sector
Sectors
Subsectors
End-use
Category of Final Energy Demand (FED)
Fossil Fuels
Modern Biomass
Electricity Heat Pump
Electricity
Traditional Fuels
Solar Thermal
Industry
Transport
Service
Household
Personal Services and others
Commercial and turism
            7.1.1. The Service Sector, Subsectors, End-use and Final Energy Demands
Motive Power
Electricity Specific Uses
Public administration
Finance and Business
Thermal Uses
District Heating
Space Heating
Air Conditioning
Notes: The service sector is divided into four sub-sectors called Commercial and Turism, Public Administration, Finance and Business and Personal Services and others.

## Slide 4: Lecture 7.1 Service sector
7.1.2. Raw Data Service Sector and Driving Parameters
4
We need to define the type of Service subsector – in this example they are 4 as defined on the left
Total floor area
total population
fraction total population in the labour force
fraction labour force in the service sector
average floor area per employee

## Slide 5: Lecture 7.1. Service Sector
            7.1.3. Space Heating Raw Data
5
We need to define Low Rise Buildings, COP Heat Pumps and Solar Thermal Share
Source: https://www.freepik.com/free-photo/3d-rendering-ventilation-system_22894132.htm#query=space%20heating&position=33&from_view=search&track=ais, Freepik</a>
Notes: To calculate the Useful Energy Demand for Space Heating we need to gather some raw data on the Floor Area (%) requiring space heating and the % of area actually heated. Also, we need to know the Low Rise Building percentage, the COP Heat Pumps Ratio and the Share of Solar Thermal.

## Slide 6: Lecture 7.1 Service sector
            7.1.4. Space Heating Reconstruction and Formulas
6
total area of the service sector
Fraction total area to be heated
specific energy consumption per area heated
Source: https://www.freepik.com/free-photo/3d-rendering-ventilation-system_22894132.htm#query=space%20heating&position=33&from_view=search&track=ais, Freepik</a>
Notes: The Useful Energy Demand for Space Heating end-use is calculated multiplying the total area of the service sector, the fraction of that area that needs to be warmed up and the specific energy consumption per area heated.
In general, space heating is needed only during the winter months; in MAED a factor called Degree-Day is defined to represent this seasonal behavior.
The degree day coefficient is defined as the sum over those months when the average temperatures is less than 18 degrees Celsius, or the difference between 18 degree Celsius and the monthly average temperature (M.A.T.), multiplied by the number of days per month (N.D.m.). Heating is only required for those months when the average temperature is less than 18 degrees Celsius.

## Slide 7: Lecture 7.1 Service sector
7.1.5. Final energy demand: electricity use for space heating
useful energy demand for heating
market penetration of electricity for heating
market penetration of heat pumps for heating
coefficient of performance of heat pumps where
Example:
25% of space heating with electricity is provided by heat pumps with COP = 4: one unit of electricity energy input gives 4 units of heat energy
So for 25% of the required useful energy demand (heat), 75% less final energy is required relative to an efficiency 1 with electricity
The final energy demand is reduced by a fraction
7
Notes: When converting useful energy demand for space heating into final energy demand for the electricity energy carrier, the fraction of that useful energy requirement which is met by heat pumps should be considered.
In MAED, electricity is assumed to have an efficiency of 1. However, heat pumps often have an efficiency, which in this context is called the coefficient of performance (C.O.P.), larger than 1. Coefficients of performance can typically range from 3 to 5. For heat pumps, the coefficient of performance is the ratio of the number of units of energy obtained in heat output and the number of units of energy inputted. This means that when using heat pumps, one unit of electricity inputted yields more than one unit of heat energy.
When calculating the final energy demand for space heating using electricity, we use the usual formula taking into account the market penetration of electricity for heating, but reduce the total amount by a fraction highlighted in red on the slide.
For example, if 25 percent of space heating useful energy demand is provided by heat pumps with coefficient of performance equal to 4 (meaning with one unit of electricity energy input giving 4 units of heat energy), 25 percent of the total required useful energy demand for heat requires 75 percent less final energy relative to an efficiency 1 with electricity. The total final energy demand is therefore reduced by the market penetration of heat pumps (M) multiplied by the difference between the coefficient of performance and 1, divided by the coefficient of performance. In this example, that is one over four times three over four, which equals three over sixteen.
This concludes lecture 7 on the sectors of MAED-D.

## Slide 8: Lecture 7.2 Other Service End-uses
            7.2.1. Air Conditioning Raw Data
8
Source: https://www.freepik.com/free-photo/close-up-ventilation-system_25777554.htm#query=air%20conditioning%20office&position=5&from_view=search&track=ais, Freepik</a>
We need to define the Floor Area (%) with Air Conditioning and the Specific Cooling Requirements.
Notes: To calculate the Useful Energy Demand for Air conditioning we need to gather some raw data on the Floor Area (%) requiring air conditioning and the specific cooling requirements.

## Slide 9: Lecture 7.2 Other Service End-uses
            7.2.2. Air Conditioning Reconstruction and Formulas
9
Useful energy demand for air conditioning:
total area of the service sector
Fraction total area to be cooled
specific energy consumption per area cooled
Source: https://www.freepik.com/free-photo/close-up-heat-pump-outside-home_22118722.htm#query=heat%20pump&position=24&from_view=search&track=ais, Freepik</a>
Notes: The Useful Energy Demand for Air conditioning end-use is calculated multiplying the total area of the service sector, the fraction of that area that needs to be cooled down and the specific energy consumption per area cooled.

## Slide 10: Lecture 7.2 Other Service End-uses
            7.2.3. Appliances and Lightning Raw Data
10
Notes: Electricity for specific uses and lighting is calculated directly as final energy demand.
Electricity for specific uses equals the total number of dwelling times the fraction of dwelling with electricity multiplied by the specific electricity consumption per dwelling. The equation for lighting is the same.
Using the fraction of electrified dwellings, the fraction of non-electrified dwellings is used to obtain the final energy demand for fossil fuels used for appliances in non-connected households.

## Slide 11: Lecture 7.2 Other Service End-uses
            7.2.4. Appliances and Lightning Reconstruction and Formulas
11
Final electricity demand for specific uses and lighting
Final fossil fuel demand for appliances
: number of households [household]
Fraction of households with electricity [-]
Specific electricity/fossil fuel consumption [energy/household]
Notes: Electricity for specific uses and lighting is calculated directly as final energy demand.
Electricity for specific uses equals the total number of dwelling times the fraction of dwelling with electricity multiplied by the specific electricity consumption per dwelling. The equation for lighting is the same.
Using the fraction of electrified dwellings, the fraction of non-electrified dwellings is used to obtain the final energy demand for fossil fuels used for appliances in non-connected households.

## Slide 12: Lecture 7.2 Service sector
7.2.5. Final energy demand
Electricity
Motor fuels
Other: Final energy demand (FED) for energy carrier and end-use , from Useful Energy Demand (UED)
, Energy intensity of specific uses electricity/motor fuels in subsector
value added of subsector
market penetration of energy carrier for end-use
efficiency of energy carrier for end-use
12
Notes: Specific uses of electricity for appliances and motor fuels for motive power are also calculated by subsector. In this case, they are calculated directly in terms of final energy demand. Equations are of the same form. Final energy demand for electricity or motor fuels equals energy intensity of electricity or motor fuels in each subsector times the value added of each subsector. Total final energy demand in the service sector for specific uses of electricity and motor fuels are found adding up the contribution of each subsector.
For uses where the useful energy demand was obtained, that useful energy is then converted into final energy, taking into account the penetration of each energy carrier into the market and the efficiency of each alternative energy source. Market penetration and efficiencies are specified as scenario parameters.
It should be mentioned that all the efficiencies in the MAED model are expressed in relative terms versus the efficiency of electricity for the same end-use.
For example, the final energy demand for modern biomass for space heating equals the useful energy demand for space heating times the market penetration of modern biomass for space heating, times the inverse of the efficiency of space heating with biomass.
For space heating, heat pumps can be used. In this case, they are included in the equation of electricity using their coefficient of performance.

## Slide 13
13
Lecture 7.3 Transportation sector
Sectors
Subsectors
End-use
Category of Final Energy Demand (FED)
Electricity
Steam Coal
LPG
Jet Fuel
Diesel
Gasoline
Industry
Transport
Service
Household
Transportation of passengers (passenger-km)
            7.3.1. The Transport Sector, Subsectors, End-use and Final Energy Demands
Car
Bus
Freight (ton-km)
International
Plane
CNG
Train
Truck
Intercity
Urban
Alcohol
Notes: In MAED, the energy demand of the transportation sector is calculated directly in terms of final energy, as a function of the total demand for transportation of passengers, freight, and international travel.
For the transport of passengers, a distinction is made for urban and intercity transport.
The fuels are user defined as needed. Each mode is defined for a single type of fuel. For example, gasoline, diesel cars, and electric cars should be defined as three different modes to allow separate fuel type calculations.
Each transport mode has a fuel associated.
International and other miscellaneous fuel consumption in transport is calculated as a linear function of total G.D.P.. Coefficients are found fitting historical data.
The energy demand is met by competing modes such as car, bus, plane, truck, train, etc. The specific energy needs, and load factors of each mode, are specified. For passenger transportation in urban and intercity, and for freight transportation, at least one transport mode must be defined..
Final Energy demand is a function of the total demand for transportation (passengers, freight, international)
Transport of passengers is split between urban (intracity), and Intercity
International/other energy in transport is calculated as a linear function of total GDP fitting historical data
Energy demand is met by competing modes, each with specified fuel type, energy intensity, and load factor

## Slide 14: Lecture 7.3 Transportation sector
7.3.2. Urban transportation
  The urban passenger transportation demand in passenger-km is:
The demand [passenger-km] is then split into modes
In turn the final energy demand for urban transport is obtained as
14
Population living in large cities
Average distance travelled by a person living in a large city
Share of mode [-]
Energy intensity of mode [energy/km]
Load factor of mode [passenger/vehicle]
N.B. Final Energy Demand is measured in energy units, while Urban Passenger Demand is in passenger kilometres (p-km)
Notes: Urban travel in MAED is considered as the travel of people living in large cities, (where public transportation exists or could be considered in the future) and trips that are done as part of one’s normal daily routine, (for example, daily commute to work).
Urban passenger transportation demand is calculated as a function of the population living in large cities and the average distance travelled per person.
The urban demand is then split into modes i as the product total urban passenger kilometre multiplied by the share of urban mode i.
Each urban transportation mode has assigned a fuel type and a specific energy intensity, which is expressed in energy units per 100 kilometres.
The total energy demand is a function of the energy intensity of urban transportation modes i in energy unit per kilometer and the load factor of each transportation mode.

## Slide 15: Lecture 7.3 Transportation sector
7.3.3. Intercity transportation: traffic activity (Raw Data)
  Total intercity travel activity [passenger-km]:
  Intercity travel activity by cars [passenger-km]:
  Intercity travel activity by public modes [passenger-km]:
    Total population
Average distance travelled/person/year
Average distance travelled/person/year by car
Loading factor [person/car]
Car ownership [car/passenger]
15
Notes: Energy demand for intercity passengers is found in a similar way as it was found in urban areas.
First, the user provides data on the average distance travelled by a person per year. The travel activity in passenger-km is obtained using demography data.
The total intercity traffic activity equals the total population multiplied by the average distance travelled by a person per year.
The share of the traffic activity covered by cars is then calculated by the product of the total population, the average intercity distance driven per car per year, the load factor for cars and the inverse of the car ownership ratio in passengers per car. The same load factor is assumed for all types of cars in intercity passenger transportation. The rest of the demand is covered by public modes.

## Slide 16: Lecture 7.3 Transportation sector
7.3.4. Intercity transportation: energy demand
The final energy consumption per mode is obtained as
is the energy intensity of mode [energy/km]
is the load factor of mode [passenger/vehicle]
and the shares of demand for car and public transport by mode
16
16
Notes: The model splits the total energy demand by modes for both car and public transport, using proportions given by the user.
Each transportation mode has assigned a fuel type, specific energy consumption or energy intensity, and loading factor given by the user in energy units per km.
Summing over all modes for both car and public transport, the final energy demand for intercity transportation is obtained.

## Slide 17: Lecture 7.3 Transportation sector
7.3.5. Final Energy Demand of Freight Transportation
The Final Energy Demand (FED) for the freight transport mode is calculated as:
The freight demand is calculated as function of Value added of the economic sectors producing goods that need to be transported (Agriculture, Construction, Mining, Manufacturing, Service, and Energy sector)
17
Freight demand
[t-km]
Share of mode
[-]
Energy intensity of mode
[energy/t-km]
Value added
Constant
Variable
N.B. Final Energy Demand is measured in energy units, while Freight Demand is in ton kilometres (tkm)
Notes: The energy demand for the freight transportation mode i is calculated as a function of the freight demand in ton kilometres, the share of the demand met by this transportation mode i, and the energy intensity of the respective mode, given in energy units per ton kilometre.
The total freight demand is calculated as a function of the value added of the economic sectors producing goods that need to be transported such as Agriculture, Construction, Mining, Manufacturing, Service, and the Energy sector.
The total ton kilometres of freight equals a base value (here A.i.) plus the sum across all the economic sectors of a variable (B.i.) which represents the transport activity multiplied by the value added for each respective sector. The variable B.i. is given in terms of ton kilometres per unit of value added.

## Slide 18
CCG courses (this will take you to the website link http://www.ClimateCompatibleGrowth.com/teachingmaterials)
18
Cannone, C., Collett, K.A., Charbonnier F., Ahsan A., Halloran C., Vijay,A.,Berdellans I., Hasanovic S., Gritsevskyi A,Stankeviciute L., Tot M.; Welsch M., Hirmer S., 2023. Lecture 7: "TRANSPORT AND SERVICE SECTORS, AND SCENARIOS DEFINITION IN MAED" , Energy Demands Projections with MAED (Model for Analysis of Energy Demand). Release Version 2.0. [online presentation]. Climate Compatible Growth & Programme and International Atomic Energy Agency.