## Slide 1
Energy Systems Analysis using OSeMOSYS
Introduction to Linear Programming Models
MSc. Fernando Plazas-Niño
February 2024

## Slide 2
AGENDA
LP Model
Practice Exercise
OSeMOSYS Model

## Slide 3
LP Model

## Slide 4
OPTIMIZATION
"The main task of an engineer is to apply their scientific and technological knowledge to solve technical problems, optimizing these solutions while considering the constraints and requirements imposed by materials, technological, economic, legal, environmental, and human factors.“
G. Pahl and W. Beitz

## Slide 5
MATHEMATICAL LP MODEL
Función objetivo
Restricciones
Funcionales
No negatividad

## Slide 6
EXAMPLE OF FORMULATION

## Slide 7
GRAPHICAL SOLUTION (1/7)
First quadrant

## Slide 8
GRAPHICAL SOLUTION (2/7)

## Slide 9
GRAPHICAL SOLUTION (3/7)

## Slide 10
GRAPHICAL SOLUTION (4/7)

## Slide 11
GRAPHICAL SOLUTION (5/7)

## Slide 12
GRAPHICAL SOLUTION (6/7)
Feasible region – Feasible solutions

## Slide 13
GRAPHICAL SOLUTION (7/7)

## Slide 14
Practice Exercise

## Slide 15
ELECTRICITY GENERATION ISLAND X
Annual Energy Planning for the Island
The island's electricity demand is 250 PJ.
There are two power plants on the island, one coal-fired and one natural gas-fired.
How much should each power plant produce to meet the annual electricity demand on the island at the minimum cost?
Power Plant | Decision variable for production (PJ) | Fuel requirement per unit of production (PJ/PJ) | Production cost (USD / PJ) | Fuel availability (PJ)
Coal PP | XCL | 3 | 350 | 600 (coal)
Gas PP | XGS | 2 | 300 | 300 (gas)
Table 1. Technical Data of Electricity Generation

## Slide 16
INDIVIDUAL WORK – 15 MINUTES

## Slide 17
ELECTRICITY GENERATION ISLAND X
Coal PP Production Constraint:
Gas PP Production Constraint:
Demand Constraint:
XCL+XGS ≥ 250
Formulation:
Variables:
XCL = Annual production (in PJ) for the Coal Power Plant (Coal PP)
XGS = Annual production (in PJ) for the Natural Gas Power Plant (Gas PP)
Objective function: Minimize the total production cost Minimize z = 350 * XCL + 300 * XGS
Constraint Formulation:
XCL ≥ 0, XGS ≥ 0
Demand: XCL + XGS ≥ 250
Coal availability: 3 * XCL ≤ 600
Natural gas availability: 2 * XGS ≤ 300

## Slide 18
ELECTRICITY GENERATION ISLAND X - SOLUTION USING GLPK
Alternative:
Use one text file for the model and another for the data.
Command line:
> glpsol
-m Isla_model.txt
-d Isla_data.txt
-o Isla_results.txt
# Set and Problem declaration
set PP;
# Parameter definition
param freq {i in PP};
param cop {i in PP};
param fav {i in PP};
# Variable description
var x {i in PP} >=0;
# Objective function
minimize z: sum{i in PP} cop[i]*x[i];
# Constraint Specification
s.t. Fuel {i in PP}: freq[i]*x[i]<= fav[i];
s.t. Demand : sum{i in PP} x[i]>=250;
# Solve statement
solve;
# End statement
end;
# Data section
data;
# Set Defintion
set PP:=
coal
gas;
# Fuel Requirement info
param freq :=
coal 3
gas 2;
# Cost of production info
param cop:=
coal 350
gas 300;
# Fuel Availability info
param fav:=
coal 600
gas 300;
# End statement
end;
Model file
Data file

## Slide 19
OSeMOSYS model

## Slide 20
SIMPLIFIED MATHEMATICAL MODEL
Welcome to the OSeMOSYS’ documentation! — OSeMOSYS 0.0.1 documentation
Languages: GNU MathProg, Python and GAMS

## Slide 21
WHAT DOES OSEMOSYS DO?
Determine the configuration of the energy system with the minimum discounted total cost for a given time period (e.g., 2016 – 2050), considering constraints such as:
Energy supply and demand (e.g., electricity)
Cost and performance of available technologies
Emission reduction objectives and renewable energy generation
Operational limitations
Others

## Slide 22
SETS, PARAMETERS AND VARIABLES
Sets
REGION
Parameters
Discount Rate
Variables
New Capacity
YEAR
TIMESLICES
EMISSIONS
COMMODITY
TECHNOLOGY
MODE OF OPERATION
Residual Capacity
Year Split
Accumulated Annual Demand
Specified Annual Demand
Input / Output Activity Ratios
Capital, fixed, variable costs
Emission Activity Ratio
Availability / Capacity Factors
Constraints (Min/Max Capacity, Total Annual/Model Period, Lower/ Upper Activity Limits, etc…)
Total Annual Capacity
Total Annual Production by Technology
Annual Emissions
Annual Technology Emissions
Discounted Capital/Operating Costs
Model Period Discounted Cost
Total Technology Annual Activity
Use by Technology Annual

## Slide 23
SETS IN OSEMOSYS
The 'Sets' define the physical structure of a model, typically independent of the specific scenarios that will be run.
They define the time domain and the time division, spatial coverage, technologies, and energy vectors to be considered, etc.
Sets
(Conjuntos)
REGION
YEAR
TIMESLICES
EMISSIONS
COMMODITY
TECHNOLOGY
MODE OF OPERATION

## Slide 24
PARAMETERS IN OSEMOSYS
The 'Parameters' are used to characterize technologies and their processes.
A set of parameters and their input data are what distinguish one technology from others, as well as its position in the model's structure.
They are also used to characterize exogenous demands, emissions, and general assumptions (e.g., discount rate, time partitions).
Parameters
Discount Rate
Residual Capacity
Year Split
Accumulated Annual Demand
Specified Annual Demand
Input / Output Activity Ratios
Capital, fixed, variable costs
Emission Activity Ratio
Availability / Capacity Factors
Constraints (Min/Max Capacity, Total Annual/Model Period, Lower/ Upper Activity Limits, etc…)

## Slide 25
TRENDS IN ESMs
Trayectorias de descarbonización
(Balyk et al., 2019; Burandt et al., 2019; Carvajal & Li, 2019; Chiodi et al., 2013; Dedinec et al., 2016; Ekins et al., 2011; Godínez-Zamora et al., 2020)
Sistemas basados en bioenergía
(Börjesson et al., 2015; Chiodi et al., 2015; Younis et al., 2020)
Rol de tecnologías
(Kato & Kurosawa, 2021; Hainoun et al., 2010; Yangka & Diesendorf, 2016)
Sistema energético 100% renovable
(Azzuni et al., 2020; Lawrenz et al., 2018; Limpens et al., 2020; Osorio-Aravena et al., 2020)
Seguridad energética
(Hainoun et al., 2010, Glynn et al., 2014, Anwar, 2016, Watts & Martinez, 2012)

## Slide 26
Integrated Assessment Models (IAMs)

## Slide 27
GDP
Population
Policies
Other assumptions
Economy
Energy system
Land and wáter systems
Climate
Economic results
Emissions
Energy mix
Land and water uses
IAMs
Source: Adapted from Carbon Brief, 2018

## Slide 28
CLIMATE, LAND, WATER, ENERGY, ECONOMY NEXUS
 | Climate | Land | Water | Energy | Economy
Climate |  | Precipitations | Precipitations | Renewable energy potential | Attention to climate change consequences
Land | CO2 absortion, GHG emissions |  | Pollution | Biomass to energy | Exports/Imports
Water |  | Water for agriculture |  | Hydroelectric plants, water for cooling, hydrogen generation | 
Energy | GHG emissions | Energy for agriculture | Pollution, energy for water treatment and management |  | Exports/Imports
Economy |  | Investment, credit, subsidies | Investment, credit, subsidies | Investment, credit, subsidies | 
Source: Adapted from Ramos et al., 2022